## Slide 1: By: Gemmachis Teshite (Ass. Prof) CCI
Chapter Five
Real Time Operating Systems

## Slide 2: Outline
4.1: Introduction
What is an Operating System
Real Time System
Types of Real time Systems
Real Time Operating System
Types of RTOS
RTOS and Embedded Systems
When to use RTOS
4.2: Context switching Mechanisms
What is Context Switching?
When to switch?
Interrupt service routines(ISR)
Tasks and Task States
4.3. RTOS Kernel
RTOS Kernel Functions
4.4. Scheduling Policies
Scheduling Parameters
Scheduling Algorithms in RTOS
4.5. Message passing and shared memory communications (RTOS Events)
Signal Event based communication
Message Event based communication
Semaphores
Task Interrupts
4.6. Inter-process communication(IPC)
What is IPC?
Two ways of IPC

## Slide 3: 4.1: Introduction
What is an Operating System
Real Time System
Types of Real time Systems
Real Time Operating System
Types of RTOS
RTOS and Embedded Systems
When to use RTOS

## Slide 4: 4.1 Introduction - What is an Operating System?
An operating system is a layer of software which takes care of technical aspects of a computer's operation.
It shields the user of the machine from the low-level details of the machine's operation and provides frequently needed facilities.
You can think of it as being the software which is already installed on a machine, before you add anything of your own.
Normally the operating system has a number of key elements:
    a technical layer of software for driving the hardware of the computer, like disk drives, the keyboard and the screen;
    a file system which provides a way of organizing files logically, and
    a simple command language which enables users to run their own programs and to manipulate their files in a simple way.

## Slide 5: 4.1 Introduction - What is an Operating System?
Generally, operating systems:
  Provide an abstraction over hardware
      Standard interfaces to a variety of HW
  Provide a user interface
      not required, but most do
  Provide an Application Prog’g Interface
  Manage resource sharing
      CPU, disk drives, network, sound, video,
      keyboard, mouse, ...
  Key objectives depend on OS
      e.g., Linux vs. Windows vs. PalmOS

## Slide 6: Real Time System
What is real-time?
Real Time: correctness is partially a function of time
i.e. Correctness of output depends on timing as well as result
A system is said to be Real Time if it is required to complete it’s work & deliver it’s services on time.
Example – Flight Control System, Real Time Monitors
  “Real time system means that the system is subjected to real time, i.e., response should be guaranteed within a specified timing constraint or system should meet the specified deadline.”
  All tasks in that system must execute on time.
  Therefore:
  Real time means that correctness of result depends on both functional correctness and time that the result is delivered.

## Slide 7: Types of Real Time Systems
Hard Real Time System
  Absolute deadline, beyond which answer is useless
  May include minimum time as well as maximum time
  Failure to meet deadlines is fatal
    example : Flight Control System
Soft Real Time System
  Approximate deadline
  Utility of answer degrades with time difference from deadline
  Late completion of jobs is undesirable but not fatal.
  System performance degrades as more & more jobs miss deadlines
    Example: Online Databases

## Slide 8: Definition- Real Time Operating System
A real-time operating system (RTOS) is an operating system that guarantees a certain capability within a specified time constraint.
An RTOS is an operating systems in which the maximum time from an input stimulus to an output response can be definitely determined.
It is a multitasking operating system intended for real-time applications with fixed deadlines
(real-time computing).
Such applications include embedded systems:
  programmable thermostats, household appliance controllers, industrial robots, spacecraft, industrial control, and scientific research equipment.

## Slide 9: Types of RTOS
An RTOS may be either
  event-driven or
  time-sharing.
An event-driven RTOS is a system that changes state only in response to an incoming event.
A time-sharing RTOS is a system that changes state as a function of time

## Slide 10: Role of an OS in Real Time Systems
Standalone Applications
  Often no OS involved
  Micro controller based Embedded Systems
Some Real Time Applications are huge & complex
  Multiple threads
  Complicated Synchronization Requirements
  Filesystem / Network / Windowing support
  OS primitives reduce the software design time

## Slide 11: RTOS and Embedded Systems
Embedded systems interface with the outside world through unusual interfaces such as sensors, actuators and specialized communication links(not using mouse, keyboard and graphic user interface).
Real-time and embedded systems operate in constrained environments in which computer memory and processing power are limited.
They often need to provide their services within strict time deadlines to their users and to the surrounding world.
It is these memory, speed and timing constraints that dictate the use of real-time operating systems in embedded software.

## Slide 12: When to use RTOS
Large projects benefit from using an RTOS
  Standardized system functions makes coding easier
    (task switching, task communication, etc.)
  Tasks makes large systems more modular and easier to debug
  Generally when a system has a dozen or more tasks that all have timing constraints

## Slide 13: Contd.
Ultra-compact systems may be better off without using an RTOS
  Small systems are easier to code from scratch and can incorporate processor optimizations, making the system more efficient than one using RTOS
  A full-featured RTOS may not fit within the size limits of an ultra-compact system.

## Slide 14: 4.2: Context switching Mechanisms
What is Context Switching?
When to switch?
Interrupt service routines(ISR)
Tasks and Task States

## Slide 15: 4.2 Context switching Mechanisms 4.2.1 What is Context Switching?
Context switching is the process of saving and restoring sufficient information for a real-time task so that it can be resumed after being interrupted.
The context is ordinarily saved to a stack data structure.
This enables multiple processes to share a single CPU.
The context switch is an essential feature of a multitasking operating system.
What constitutes the context is determined by the processor and the operating system.

## Slide 16: Context Switching…
Switching from one process to another requires a certain amount of time for doing the administration.
  saving and loading registers and memory maps, updating various tables and list etc.
Context switching time is a major contributor to response time and therefore must be minimized.
The rule for saving context is simple:
  save the minimum amount of information necessary to safely restore any process after it has been interrupted.

## Slide 17: Context switching….
A context switch can mean:
  a register context switch,
  a task context switch,
  a thread context switch, or
  a process context switch.
That is, Context usually includes:
  contents of general registers
  contents of the program counter
  contents of coprocessor registers (if present)
  memory page register
  images of memory-mapped I/O locations (mirror images)
Interrupts are disabled during context-switching.
  Sometimes a partial context switch is used to handle a burst of interrupts, to detect spurious interrupts, or to handle a time-overloaded condition.

## Slide 18: Context switching….
The stack model for context switching is used mostly in embedded systems where the number of real-time or interrupt-driven tasks is fixed.
In the stack model, each interrupt handler is associated with a hardware interrupt and is invoked by the CPU, which vectors to the instruction stored at the appropriate interrupt-handler location.
The context is then saved to a specially designated memory area that can be static, in the case of a single-interrupt system, or a stack, in the case of a multiple-interrupt system.

## Slide 19: 4.2.2 When to switch?
There are three situations where a context switch needs to occur. They are:
1. Multitasking
Most commonly, within some scheduling scheme, one process needs to be switched out of the CPU so another process can run. This context switch can be triggered by the process making itself unrunnable, such as by waiting for an I/O or synchronization operation to complete.
On a pre-emptive multitasking system, the scheduler may also switch out processes which are still runnable. To prevent other processes from being starved of CPU time, preemptive schedulers often configure a timer interrupt to fire when a process exceeds its time slice. This interrupt ensures that the scheduler will gain control to perform a context switch.

## Slide 20: When to switch?
2. Interrupt handling
Modern architectures are interrupt driven.
This means that if the CPU requests data from a disk, for example, it does not need to busy-wait until the read is over; it can issue the request and continue with some other execution.
When the read is over, the CPU can be interrupted and presented with the read.
For interrupts, a program called an interrupt handler is installed, and it is the interrupt handler that handles the interrupt from the disk.

## Slide 21: When to switch?
3. User and kernel mode switching
When a transition between user mode and kernel mode is required in an operating system, a context switch is not necessary; a mode transition is not by itself a context switch. However, depending on the operating system, a context switch may also take place at this time.

## Slide 22: 4.2.3 Interrupt service routines(ISR)
Hardware interrupt - a signal generated by a peripheral device and sent to the CPU. The trigger is an electrical signal from an external device.
    Hardware interrupts are asynchronous in nature.
Software interrupt - similar to the hardware interrupt, and it causes one code module to pass control to another. Trigger of this is the execution of a machine language instruction.
An exception is a software interrupt that is internal to the CPU and triggered by a software program's attempt to perform an unexpected or illegal operation.
All three interrupts cause the CPU to transfer execution to a known location and then execute an interrupt service routine (ISR).

## Slide 23: 4.2.4 Tasks and Task States
Application software is split up into multitasking blocks called ‘Tasks’.
Tasks are generic computational blocks with:
  Timing constraints
  Synchronization and
  communication relationships with other tasks
A task – a simple subroutine
Generally each device is represented by its own task.
Embedded Systems application makes calls to the RTOS functions to start tasks, passing to the OS, start address, stack pointers, etc. of the tasks

## Slide 24: Tasks and Task States…
Task States:
  Running,
  Ready (possibly: suspended, pended), and
  Blocked (possibly: waiting, dormant, delayed)
Scheduler schedules/shuffles tasks between Running and Ready states
Blocking is self-blocking by tasks, and moved to Running state via other tasks’ interrupt signaling
  when block-factor is removed/satisfied
When a task is unblocked with a higher priority over the ‘running’ task, the scheduler ‘switches’ context immediately.

## Slide 26: Contd.
Tasks can be in one of four states
  SLEEPING
  READY
  RUNNING
  BLOCKED

## Slide 27: Contd.
Ways to move between tasks:
  SLEEPING  READY
    through an RTOS system function called from a different task.
  READY  RUNNING
    from being selected for execution by the RTOS. There can only be one RUNNING task at a time.
  RUNNING  BLOCKED
    when the task is told to wait for an event to occur.
  BLOCKED  RUNNING
    After the event, a task has been waiting for occurs and has higher priority than current RUNNING task.
  RUNNING  SLEEPING
    once task has finished execution.

## Slide 28: The task control block model
Each task is associated with a data structure –
  a task control block (TCB).
TCB contains context.
The system stores TCBs in one or more data structures, such as a linked list.
TCB model can be used in:
  round-robin,
  preemptive priority or
  combination systems, although it is generally associated with round-robin systems with a single clock.
The operating system manages TCBs by keeping track of the status of each task.

## Slide 29: The task control block model
Every hardware interrupt and every system level call (such as a request on a resource) invokes the real-time operating system.
The operating system is responsible for:
  maintaining a linked list containing the TCBs of all the ready tasks, and
  a second linked list of those in the suspended state.
It also keeps:
  a table of resources and
  a table of resource requests.

## Slide 30: 4.3. RTOS Kernel
RTOS Kernel Functions

## Slide 31: 4.3 RTOS Kernel
RTOS Kernel provides an Abstraction layer that hides from application software and the hardware details of the processor or set of processors upon which the application software shall run.
They are often called a kernel or executive process, not a full-blown Operating System.
Application Software
RTOS
Hardware

## Slide 32: 4.3.1 RTOS Kernel Functions

## Slide 33: 4.3.1.1 Task Management
It is the most basic category of kernel services, at the very center .
These set of services are used to allow application software developers to design their software as a number of separate chunks of software each handling:
  a distinct topic,
  a distinct goal, and
  perhaps its own real-time deadline.

## Slide 34: 4.3.1.1 Task Management
Each separate “chunk” of software is called a “task”.
Services in this category include the ability to launch tasks and assign priorities to them.
Main service offered is Task Scheduling
  controls the execution of application software tasks
  can make them run in a very timely and responsive fashion.

## Slide 35: Task Scheduling
Non Real-time systems usually use Non-preemptive Scheduling
  Once a task starts executing, it completes its full execution.
Most RTOS perform priority-based preemptive task scheduling.
Basic rules for priority based preemptive task scheduling
  The Highest Priority Task that is Ready to Run, will be the Task that Must be Running.
  Preemptive permits one task to preempt another one of lower priority
Priority based Preemptive Task Scheduling
Every Task in a software application is assigned a priority.
Higher Priority = Higher Need for Quick Response.
Follows nested preemption

## Slide 36: Real-Time Task
Task : a sequence of similar jobs
  Periodic task (p,e)
    Its jobs repeat regularly
    Period p = inter-release time (0 < p)
    Execution time e = maximum execution time (0 < e < p)
    Utilization U = e/p
5
10
15
0

## Slide 37: 4.4. Scheduling Policies
Scheduling Parameters
Scheduling Algorithms in RTOS

## Slide 38: 4.4 Scheduling Policies
Features of RTOS’s
  Scheduling.
  Resource Allocation.
  Interrupt Handling.
  Other issues like kernel size.
More information about the tasks are known
  Number of tasks
  Resource Requirements
  Release Time
  Execution time
  Deadlines

## Slide 39: 4.4.1 Scheduling Parameters
Assume N CPUs available for execution of a single task set
Set of tasks {Ti}
  Periods pi
  Deadline di (completion deadline after task is queued)
  Execution time ci (amount of CPU time to complete)
Handy values:
  Laxity li = di – ci
  (amount of slack time before Ti must begin execution)
  Utilization factor ui = ci/pi
  (portion of CPU used)

## Slide 40: 4.4.2 Scheduling Algorithms in RTOS
Clock Driven Scheduling
Weighted Round Robin Scheduling
Priority Scheduling

## Slide 41: 1. Clock Driven
All parameters about jobs known in advance.
  release time
  execution time
  deadline
Schedule can be computed offline or at some regular time instances.
Advantage
  Minimal runtime overhead.
Disadvantage
  Not suitable for many applications.

## Slide 42: 2. Weighted Round Robin
Jobs scheduled in FIFO manner
Time quantum given to jobs is proportional to its weight.
Example use:
  High speed switching network
  QOS guarantee.
Disadvantage:
  Not suitable for precedence constrained jobs.
  Job A can run only after Job B. No point in giving time quantum to Job B before Job A.

## Slide 43: 3. Priority Scheduling
(Greedy/List/Event Driven)
  Processor never left idle when there are ready tasks
  Processor allocated to processes according to priorities
  Priorities can be:
  Static-priority algorithm (Rate Monotonic)
    - done at compile time for all possible tasks
  Dynamic-priority algorithm (Earliest Deadline First)
      computed at run-time based on tasks really executing

## Slide 44: 4.5. Message passing and shared memory communications (RTOS Events)
Signal Event based communication
Message Event based communication
Semaphores
Task Interrupts

## Slide 45: 4.5 Message passing and shared memory communications (RTOS Events)
Events can be used by tasks to communicate between each other or to help coordinate execution flow.
Four common RTOS events:
  Signals
  Messages
  Semaphores
  Interrupts

## Slide 46: 4.5.1 Signal Event Based Communication
Signaling is the fastest method of communication.
No actual information is exchanged, a signal is simply a single-bit flag.
It is important for coordinating execution flow amongst tasks.
Only one signal can be saved per task, and any extra signals are ignored.

## Slide 47: Contd.
void task1 (void) _task_ 1 {
...
os_send_signal (2); // signal task 2
os_clear_signal (1); // clear task 1 flag
os_wait (K_SIG, 0, 0); // wait for signal
...
}
Tasks can send and clear signal for any other task, including itself.
Tasks waiting for signal are BLOCKED. The RTOS unblocks that task once the event is received.

## Slide 48: 4.5.2 Message Event Based Communication
A message is a set of data that gets transferred through message queues or mailboxes.
Tasks which send messages are BLOCKED until the message can be sent or timeout occurs.
  int message
  / send data in variable ‘message’ to mailbox 2;
  // timeout after 10 machine cycles
  os_send_message (2, message, 10);
Tasks can wait for messaging event and store the message to variable.
  // wait for message in mailbox 3 and store
  // in &message; or timeout in 10 machine cycles
  os_wait (K_MBX + K_TMO + 3, 10, &message);

## Slide 49: 4.5.3 Semaphores
Semaphores help prevent resource sharing conflicts between tasks.
A semaphore is a way to lock a resource so that it is guaranteed that while a piece of code is executed, only this piece of code has access to that resource.
This keeps two threads from concurrently accessing a resource, which can cause problems.

## Slide 50: Semaphores…
A semaphore is an object containing a natural number (i.e. a integer greater or equal to zero) on which two modifying operations are defined.
  One operation, V, adds 1 to the natural.
  The other operation, P, decreases the natural number by 1.
  Both activities are atomic
    (i.e. no other operation can be executed at the same time as a V or a P).
It's simply a way to limit the number of consumers for a specific resource.
  For example, to limit the number of simultaneous calls to a database in an application.

## Slide 51: 4.5.4 Task Interrupts
Each interrupt source can only be assigned to one task.
Multiple interrupts can be assigned to a single task.
Attaching an interrupt does not automatically set the corresponding interrupt enable flag.
In fact, the relevant flags are only enabled when tasks begin to wait for an interrupt event.

## Slide 52: 4.6. Inter-process communication(IPC)
What is IPC?
Two ways of IPC

## Slide 53: 4.6 Inter-process communication(IPC) 4.6.1 What is IPC?
Tasks must be able to communicate with one another to coordinate their activities to share the data.
IPC means that a process (scheduler, task or ISR) generates some information by setting or resetting a flag or value, or generates an output so that it lets another process take note of it or use it.
IPCs in multiprocessor system are used to generate information about certain sets of computations finishing on one processor and let the other processors take note of it.

## Slide 54: 4.6.2 Two ways for IPC
Global data ,
Sending messages
4.6.2.1. Global data: by setting global variables.
Usage of global variables create two problems.
      Shared data problem
      It cannot prevent a message from being accessed by other tasks
4.6.2.2. Sending messages
Semaphores and mutexes
Queues, pipes and mailboxes
Signals
Event registers etc.

## Slide 55: 4.6.2.2. 1 Mailboxes
Mailboxes are also called as message exchange, is typically a pointer size variable
A message mailbox is an IPC message-block that can be used only by a single destined task.
Through a service provided by the kernel, a task or an ISR can deposit a message into the mail box.

## Slide 56: Mailboxes…
Similarly, one or more tasks can receive messages through a service provided by the kernel.
A waiting list is associated with each mailbox in case more than one task wants to receive messages through the mailbox.
Tasks rely on the kernel to allow them to write to the location via a post operation or to read from it via a pend operation.
Mailboxes are available in most commercial RTOS.

## Slide 57: Mailboxes
Mailbox object is just like postal mailbox.
Task 1
Task 2
mailbox
Post a message
Read the message

## Slide 58: Mailbox services provided by the kernel
Initialize the contents of the mailbox. The mailbox may or may not contain a message.
Deposit a message into the mailbox (POST)
Wait for a message to be deposited into the mailbox (PEND)
Get a message from a mailbox if existing (ACCEPT)
A provision for one message-write per box and the next message to be accepted only if the previous one is read.
A mailbox with a provision for only one message per box becomes full with one message.

## Slide 59: Mailbox management functions
Create a mailbox -- RTOS_BoxCreate
Delete a mailbox -- RTOS_BoxDelete
Query a mailbox – RTOS_BoxQuery
Wait for a mailbox – RTOS_BoxWait
Post a message into the mail box -- RTOS_BoxWrite
Read a message from the mailbox – RTOS_BoxAccept

## Slide 60: Mailboxes
Task resource request table.
Resource table used in conjunction with task resource request table.

## Slide 61: 4.6.2.2. 2 Message queue
Message queue is used to send one or more messages to a task.
It is basically an array of mailboxes.
Waiting
Timeout option
Some operating systems support qpost, qpend, and qaccept operations.

## Slide 62: Features of message queues
Either one process (task) or a set of processes (tasks) can use the queue.
A read (deletion) operation from a queue is in a FIFO mode.
Generally the queue is a circular queue and the read is like a ring of bytes in a buffer.
For reading, one can assign priorities.

## Slide 63: Continued..
At the time of creating a queue, the queue is given a
          Name or ID
          Queue length
          Sending task waiting list
          Receiving task waiting list
Applications of message queues
  Taking the input from a keyboard
  To display the output
  Reading voltages from sensors or transducers
  Data packet transmission in a network

## Slide 64: Types
One way comm. With Ack
Two-way comm.
Broadcasting

## Slide 65: One way communication with ack
.
Task 1
Task 2
semaphore
Message queue

## Slide 66: Two way communication
.
Task 1
Task 2
Message queue

## Slide 67: Broadcasting
.
Task
Task
Message queue
Task
Task

## Slide 68: Kernel message queue services
Initialize a queue. It is always assumed to be empty after initialization.
Deposit a message into the queue (POST)
Wait for a message to be deposited into the queue (PEND)
Get a message from a queue (ACCEPT)

## Slide 69: Message queue management functions
Create a queue -- RTOS_Qcreate
Delete a queue
Flush a queue --RTOS_Qflush
Post a message in queue – RTOS_Qwrite
Post a message in front of queue -- RTOS_Qpostfront
Read message from queue -- RTOS_Qaccept
Broadcast a message
Show queue information
Show queue waiting list – RTOS_Qwait

## Slide 70: Buffering data
Mechanisms are needed to pass data between tasks in a multitasking system when production and consumption rates are unequal.
Example, one task may produce data at a constant 100 units per second, whereas another may consume these data at a rate less than 100 units per second.
  Assuming that the production interval is finite (and relatively short), the slower consumption rate can be accommodated if the producer fills a storage buffer with the data.
  The buffer holds the excess data until the consumer task can catch up.
  The buffer can be a queue or other data structure, including an unorganized mass of variables.
  If consumer task consumes this information faster than it can be produced, or if the consumer cannot keep up with the producer, problems occur.
Selection of the appropriate size buffer and synchronization mechanisms is critical in reducing or eliminating these problems.

## Slide 71: Pipes
Pipes are like message-queue functions.
A message pipe or simply pipe in strict sense is an IPC queue between two given inter-connected tasks or two sets of tasks.
Unlike queues and mailboxes, pipes have unlimited size.
In a pipe there may be no fixed number of bytes per message.
Example: client-server network.
  Task-to-task and ISR-to-task data transfer can take place using pipes.
Task
Pipe
Task
Write data to pipe
Reads data from pipe
Task

## Slide 72: Pipes for inter-process communication
Pipes can be used for inter-process communication.
One task may send the data packets through one pipe and the other task may send acknowledgements through the other
While using a pipe you have to define
        Pipe ID
        Length
        Maximum length (not defined in some RTOS)
        Initial values
Task
Task

## Slide 73: Memory Management
some embedded systems are locked away and expected to run for years on end without being rebooted.
If we use conventional memory-management schemes to control memory allocation, we can end up with fragmented memory which can take valuable time to defragment and really is a major problem for tasks that are time-sensitive.
There are a variety of ways to deal with memory:
Some systems never do a malloc() or free() -- all memory is allocated at compile time.

## Slide 74: Others
In addition to kernel services, many RTOSs offer a number of optional add-on operating system components for such high-level services as:
            file system organization,
            network communication,
            network management,
            database management,
            user-interface graphics, etc.
Although many of these add-on components are much larger and much more complex than the RTOS kernel, they rely on the presence of the RTOS kernel and take advantage of its basic services.
Each of these add-on components is included in an embedded system only if its services are needed for implementing the embedded application, in order to keep program memory consumption to a minimum.